## Slide 1: KMALLCLEAN

## Slide 2: Overview
What is KMALLClean?
Is a tool to automate the cleaning of raw MBES data in KMALL file format.
Computes a raw point cloud from the kmall file.
Uses machine learning to analyse the raw point cloud and determine the level of noise present
Cleans the largest outliers to a user-specified percentage of the file.

## Slide 3: How do we control the cleaning process?
MBES data quality can be very inconsistent across projects, vessels, terrains, weather conditions and survey line direction.
A filter configuration which works well on one file, is often not suitable for another file.
KMALLclean analyses each file and makes an assessment of the noise level.
Using the user configuration of “percentage outliers to reject”, the engine rejects the most noisy outliers in the file.
By using a percentage rather than a ‘outlier threshold’ the filter only rejects the most noisy points, not everything beyond a threshold. This is a very different approach and permits the machine learning to adapt to the data in hand
If more points are required to be rejected, a higher percentage threshold should be specified.
If less points are required to be rejected, a lower percentage threshold should be specified.
On completion of outlier selection, an NEW kmall file is created.
  The original kmall file is not modified in any way
  The new file contains the same volume of data, same datagrams
  The only modification is the beam quality flag which is set to rejected.
  The original depths remain unchanged. This means they can easily be reviewed and re-accepted in CARIS if required.

## Slide 4: How to we assess the engine performance?
We have compared the results of the engine with manual cleaning. The results are quite similar to manual cleaning, but not identical.
Testing has demonstrated manual cleaning is very inconsistent. Different processing personnel never provide identical cleaned data. Even the same person cannot repeat the same cleaned result.
A better way to assess performance is to use the QAX tool find fliers. This is used to identify outliers in the processed TIF/BAG files following data processing.
QAX will find fliers but is not 100% accurate. On steep slopes, reefs, rocky seafloor it often reports false positives. The tool needs to be used as a guide, not as an absolute validation

## Slide 5: Notes
Percent 0.1 is sensible
NN 3 is sensible
NN20 and NN10 have negligible differences
tatistical_outlier_removal removes points that are further away from their neighbors compared to the average for the point cloud. It takes two input parameters:
nb_neighbors, which specifies how many neighbors are taken into account in order to calculate the average distance for a given point.
std_ratio, which allows setting the threshold level based on the standard deviation of the average distances across the point cloud. The lower this number the more aggressive the filter will be.